## Slide 1: 3d Mapping Using Autonomous Aerial Vehicles
EECE 5698 Individual Projects
Andrew Tu

## Slide 2: Social Value
Search and Rescue
Land/Infrastructure Surveying
Exploration/Reconnaissance
Build collaborative maps with other autonomous systems
AR/VR reconstructions for various applications

## Slide 3: Power
Li-Ion Battery
Pro:
  Light weight
  High Power Density (~100-200 WH/kg)
  Fast charge time
  Higher voltages
Con:
  Combustible
  “Temperamental” in use
13000 mAh @ 12V = 155Wh or ~ 1 Hour Flight Time
(Scale as necessary)
Consumption
Total: ~155W
Notes: Lidar Spec: https://www.autonomoustuff.com/wp-content/uploads/2016/08/VLP-16-Puck.pdf
Li-Ion Battery Pro/con: http://electronics360.globalspec.com/article/5555/lithium-batteries-the-pros-and-cons
Drone Power Consumption: https://www.quora.com/What-is-the-power-consumption-of-a-drone-like-the-Phantom-DJI
https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=images&cd=&cad=rja&uact=8&ved=2ahUKEwiOzo6TpYHaAhVI3IMKHY5OBVwQjRx6BAgAEAU&url=https%3A%2F%2FwComparison: ww.homepower.com%2Farticles%2Fsolar-electricity%2Fequipment-products%2Flithium-ion-batteries-grid-systems&psig=AOvVaw0_GwwouIS0n4OH93BNYSnp&ust=1521854822303921
Types of Li-ion: http://synergyfiles.com/2015/09/5-types-of-lithium-ion-batteries/

## Slide 4: Consumption Break Down
Consumption
Flight: ~140W
Lidar: ~8W
Camera: ~.5W
Micro Processor: ~1W
Other Sensors (+ wiggle room): ~5 W
Total: ~155W
Consumption
DJI Drone M200 has 97.58 Wh battery with 30 min of Flight time -> If Li-Ion batteries can only discharge 70% of their stored energy, ~70 Wh of energy available.
70Wh * 60 min/30min = ~ 140 W
therefore, roughly 140W are spent on Flight
Veledyne (VLP-16) spec. specifies 8W.
Camera/Micro Processor measurements came from class discussions
Notes: Lidar Spec: https://www.autonomoustuff.com/wp-content/uploads/2016/08/VLP-16-Puck.pdf
Li-Ion Battery Pro/con: http://electronics360.globalspec.com/article/5555/lithium-batteries-the-pros-and-cons
Drone Power Consumption: https://www.quora.com/What-is-the-power-consumption-of-a-drone-like-the-Phantom-DJI
https://www.google.com/url?sa=i&rct=j&q=&esrc=s&source=images&cd=&cad=rja&uact=8&ved=2ahUKEwiOzo6TpYHaAhVI3IMKHY5OBVwQjRx6BAgAEAU&url=https%3A%2F%2FwComparison: ww.homepower.com%2Farticles%2Fsolar-electricity%2Fequipment-products%2Flithium-ion-batteries-grid-systems&psig=AOvVaw0_GwwouIS0n4OH93BNYSnp&ust=1521854822303921
Types of Li-ion: http://synergyfiles.com/2015/09/5-types-of-lithium-ion-batteries/

## Slide 5: Sensing
Lidar – Primary means of map generation, generate high definition point clouds of surroundings.
  Accurate to +/- 3 cm
  Range of 100M
GPS – Can be used outdoors for navigation and plotting map data on global scale
  Accurate to +/- 3 M (no RTK) outdoors in open space
  Accurate to +/- 2cm (RTK) outdoors in Open Space
  Not usable indoors or in areas with heavy obstructions
IMU – Versatile Sensor for sensor fusion. Can assist in Monocular VIO and/or used for dead reckoning
  Provides measurements for movements w/in 3D space.
Camera – Can also be used in map generation.
  Offers users FPV of drone (Either used for remote operation OR just for user friendly view)
  Data can be collected and used for post processing map generation
  Can assist in object/obstacle detection
  Good “Catch all” Sensor

## Slide 6: Navigation
SLAM w/ Lidar and/or VSLAM w/ Camera.
Outdoor Open Space: Can use GPS sensor
Fail safe: Dead Reckoning w/ IMU
Camera or Lidar used for Obstacle detection/Avoidance
Outdoor applications (Open Air Flight, No Obstructions):
  accuracy to +/- 2cm using RTK GPS
  Accuracy to +/- 2m using GPS
  Don’t need high accuracy readings since few obstacles, use normal GPS for accuracy @ +/- 2m
Outdoor Applications (Near Obstructions, More Obstacles, Forests): Accuracy to 30 cm
  Use Lidar and SLAM to estimate position in self built map
  Use GPS data when available to match position of map to global coordinate system
Indoor applications: Accuracy to 30 cm
  Use Lidar and SLAM to estimate position in self built map
  Closer quarters, more danger of ramming into things while flying

## Slide 7: System Level Design
Li-Ion Battery
Microcontroller
Propeller
Camera
GPS
IMU
LIDAR
Propeller
Propeller
Propeller

## Slide 8: software and Future Work
OS: Ubuntu 16.04
Use ROS to manage sensors
  Offers Time Synchronization of data
  Active developer community with lots of package support
Utilize OpenCV to process image data
Evaluate Google Cartographer vs Gmapping packages for SLAM + Lidar data representation